Complete list of standard values, version 2 - Public

This file gives the standard values as published on www.biograce.net in Word format. 
Two Word versions of this list exist:

- A complete list of standard values, containing all the values as listed in the Excel version

- A condensed list showing the most important standard values

This file contains the complete list.

Abbreviations and definitions used can be found in the Excel file on the web page http://www.biograce.net/content/ghgcalculationtools/standardvalues.

- Global Warming Potentials

| CO2 | 1 | g CO2,eq / g CO2 |
| --- | --- | --- |
| CH4 | 23 | g CO2,eq / g CH4 |
| N2O | 296 | g CO2,eq / g N2O |

- GHG emission coefficients

  - Agro-inputs

| N-fertiliser | 2827,0 | g CO2/kg N | 8,68 | g CH4/kg N | 9,6418 | g N2O/kg N | 5880,6 | g CO2,eq/kg N |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| P2O5-fertiliser | 964,9 | g CO2/kg P2O5 | 1,33 | g CH4/kg P2O5 | 0,0515 | g N2O/kg P2O5 | 1010,7 | g CO2,eq/kg P2O5 |
| K2O-fertiliser | 536,3 | g CO2/kg K2O | 1,57 | g CH4/kg K2O | 0,0123 | g N2O/kg K2O | 576,1 | g CO2,eq/kg K2O |
| CaO-fertiliser | 119,1 | g CO2/kg CaO | 0,22 | g CH4/kg CaO | 0,0183 | g N2O/kg CaO | 129,5 | g CO2,eq/kg CaO |
| Pesticides | 9886,5 | g CO2/kg | 25,53 | g CH4/kg | 1,6814 | g N2O/kg | 10971,3 | g CO2,eq/kg |
| Seeds- corn | - | g CO2/kg | - | g CH4/kg | - | g N2O/kg | - | g CO2,eq/kg |
| Seeds- rapeseed | 412,1 | g CO2/kg | 0,91 | g CH4/kg | 1,0028 | g N2O/kg | 729,9 | g CO2,eq/kg |
| Seeds- soy bean | - | g CO2/kg | - | g CH4/kg | - | g N2O/kg | - | g CO2,eq/kg |
| Seeds- sugarbeet | 2187,7 | g CO2/kg | 4,60 | g CH4/kg | 4,2120 | g N2O/kg | 3540,3 | g CO2,eq/kg |
| Seeds- sugarcane | 1,6 | g CO2/kg | 0,00 | g CH4/kg | 0,0000 | g N2O/kg | 1,6 | g CO2,eq/kg |
| Seeds- sunflower | 412,1 | g CO2/kg | 0,91 | g CH4/kg | 1,0028 | g N2O/kg | 729,9 | g CO2,eq/kg |
| Seeds- wheat | 151,1 | g CO2/kg | 0,28 | g CH4/kg | 0,4003 | g N2O/kg | 275,9 | g CO2,eq/kg |

  - Residues (feedstock or nput)

| EFB compost | 0,0 | g CO2/kg | 0,00 | g CH4/kg | 0,0000 | g N2O/kg | 0,0 | g CO2,eq/kg |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Filter mud cake | 0,0 | g CO2/kg | 0,00 | g CH4/kg | 0,0000 | g N2O/kg | 0,0 | g CO2,eq/kg |
| Vinasse | 0,0 | g CO2/kg | 0,00 | g CH4/kg | 0,0000 | g N2O/kg | 0,0 | g CO2,eq/kg |

  - Fuels (also conversion inputs)

| Natural gas (4000 km, Russian NG quality) | 61,58 | g CO2/MJ | 0,1981 | g CH4/MJ | 0,0002 | g N2O/MJ | 66,20 | g CO2,ew/MJ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Natural gas (4000 km, EU Mix quality) | 62,96 | g CO2/MJ | 0,1981 | g CH4/MJ | 0,0002 | g N2O/MJ | 67,59 | g CO2,ew/MJ |
| Diesel | 87,64 | g CO2/MJ | - | g CH4/MJ | - | g N2O/MJ | 87,64 | g CO2,ew/MJ |
| HFO | 84,98 | g CO2/MJ | - | g CH4/MJ | - | g N2O/MJ | 84,98 | g CO2,ew/MJ |
| HFO for marine transport | 87,20 | g CO2/MJ | - | g CH4/MJ | - | g N2O/MJ | 84,98 | g CO2,ew/MJ |
| Methanol | 92,80 | g CO2/MJ | 0,2900 | g CH4/MJ | 0,0003 | g N2O/MJ | 99,57 | g CO2,ew/MJ |
| Hard coal | 102,38 | g CO2/MJ | 0,3835 | g CH4/MJ | 0,0003 | g N2O/MJ | 111,28 | g CO2,ew/MJ |
| Lignite | 116,76 | g CO2/MJ | 0,0091 | g CH4/MJ | 0,0001 | g N2O/MJ | 116,98 | g CO2,ew/MJ |
| Wheat straw | 1,75 | g CO2/MJ | 0,0013 | g CH4/MJ | 0,0001 | g N2O/MJ | 1,80 | g CO2,ew/MJ |

  - Electricity

| Electricity EU mix MV | 119,36 | g CO2/MJ | 0,2911 | g CH4/MJ | 0,0054 | g N2O/MJ | 127,65 | g CO2,ew/MJ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Electricity EU mix LV | 120,79 | g CO2/MJ | 0,2946 | g CH4/MJ | 0,0055 | g N2O/MJ | 129,19 | g CO2,ew/MJ |

  - Electricity production (reference for credit calculation)

| Electricity (NG CCGT) | 114,48 | g CO2/MJ | 0,3679 | g CH4/MJ | 0,0050 | g N2O/MJ | 9,94 | g CO2,ew/MJ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Electricity (Lignite ST) | 284,77 | g CO2/MJ | 0,0259 | g CH4/MJ | 0,0078 | g N2O/MJ | 2,90 | g CO2,ew/MJ |
| Electricity (Straw CHP) | 5,56 | g CO2/MJ | 0,0042 | g CH4/MJ | 0,0002 | g N2O/MJ | 0,15 | g CO2,ew/MJ |

  - CH4 and N2O emissions of steam production

| CH4 and N2O emissions, steam from NG boiler | - |  | 0,0028 | g CH4/MJ | 0,0011 | g N2O/MJ | 0,39 | g CO2,ew/MJ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CH4 and N2O emissions, steam from Lignite CHP | - |  | 0,0023 | g CH4/MJ | 0,0126 | g N2O/MJ | 3,79 | g CO2,ew/MJ |

  - Conversion inputs

| n-Hexane | 80,08 | g CO2/MJ | 0,0146 | g CH4/MJ | 0,0003 | g N2O/MJ | 80,50 | g CO2,ew/MJ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Phosphoric acid (H3PO4) | 2776,0 | g CO2/kg | 8,93 | g CH4/kg | 0,1028 | g N2O/kg | 3011,7 | g CO2,eq/kg |
| Fuller's earth | 197,0 | g CO2/kg | 0,04 | g CH4/kg | 0,0063 | g N2O/kg | 199,7 | g CO2,eq/kg |
| Hydrochloric acid (HCl) | 717,4 | g CO2/kg | 1,13 | g CH4/kg | 0,0254 | g N2O/kg | 750,9 | g CO2,eq/kg |
| Sodium carbonate (Na2CO3) | 1046,0 | g CO2/kg | 6,20 | g CH4/kg | 0,0055 | g N2O/kg | 1190,2 | g CO2,eq/kg |
| Sodium hydroxide (NaOH) | 438,5 | g CO2/kg | 1,03 | g CH4/kg | 0,0240 | g N2O/kg | 469,3 | g CO2,eq/kg |
| Potassium hydroxide (KOH) | 0,0 | g CO2/kg | 0,00 | g CH4/kg | 0,0000 | g N2O/kg | 0,0 | g CO2,eq/kg |
| Hydrogen (for HVO) | 80,87 | g CO2/MJ | 0,2765 | g CH4/MJ | 0,0003 | g N2O/MJ | 87,32 | g CO2,ew/MJ |
| Pure CaO for processes | 1013,0 | g CO2/kg | 0,65 | g CH4/kg | 0,0076 | g N2O/kg | 1030,2 | g CO2,eq/kg |
| Sulphuric acid (H2SO4) | 193,9 | g CO2/kg | 0,55 | g CH4/kg | 0,0045 | g N2O/kg | 207,7 | g CO2,eq/kg |
| Ammonia | 2478,0 | g CO2/kg | 7,84 | g CH4/kg | 0,0087 | g N2O/kg | 2660,8 | g CO2,eq/kg |
| Cycle-hexane | 723,0 | g CO2/kg | 0,00 | g CH4/kg | 0,0000 | g N2O/kg | 723,0 | g CO2,eq/kg |
| Lubricants | 947,0 | g CO2/kg | 0,00 | g CH4/kg | 0,0000 | g N2O/kg | 947,0 | g CO2,eq/kg |

- Fossil energy input

  - Agro-inputs

| N-fertiliser | 48,99 | MJfossil/kg N |
| --- | --- | --- |
| P2O5-fertiliser | 15,23 | MJfossil/kg P2O5 |
| K2O-fertiliser | 9,68 | MJfossil/kg K2O |
| CaO-fertiliser | 1,97 | MJfossil/kg CaO |
| Pesticides | 268,40 | MJfossil/kg |
| Seeds- corn | - | MJfossil/kg |
| Seeds- rapeseed | 7,87 | MJfossil/kg |
| Seeds- soy bean | - | MJfossil/kg |
| Seeds- sugarbeet | 36,29 | MJfossil/kg |
| Seeds- sugarcane | 0,02 | MJfossil/kg |
| Seeds- sunflower | 7,87 | MJfossil/kg |
| Seeds- wheat | 2,61 | MJfossil/kg |
| EFB compost | 0,00 | MJfossil/kg |

  - Residues (feedstock or input)

| EFB compost | 0,00 | MJfossil/kg |
| --- | --- | --- |
| Filter mud cake | 0,00 | MJfossil/kg |
| Vinasse | 0,00 | MJfossil/kg |

  - Fuels (also conversion inputs)

| Natural gas (4000 km, Russian NG quality) | 1,1281 | MJfossil/MJ |
| --- | --- | --- |
| Natural gas (4000 km, EU Mix quality) | 1,1281 | MJfossil/MJ |
| Diesel | 1,16 | MJfossil/MJ |
| HFO | 1,088 | MJfossil/MJ |
| HFO for marine transport | 1,088 | MJfossil/MJ |
| Methanol | 1,6594 | MJfossil/MJ |
| Hard coal | 1,0886 | MJfossil/MJ |
| Lignite | 1,0156 | MJfossil/MJ |
| Wheat straw | 0,0254 | MJfossil/MJ |

  - Electricity

| Electricity EU mix MV | 2,6951 | MJfossil/MJ |
| --- | --- | --- |
| Electricity EU mix LV | 2,7275 | MJfossil/MJ |

  - Electricity production (reference for credit calculation)

| Electricity (NG CCGT) | 2,0511 | MJfossil/MJ |
| --- | --- | --- |
| Electricity (Lignite ST) | 2,4770 | MJfossil/MJ |
| Electricity (Straw CHP) | 0,0806 | MJfossil/MJ |

  - Conversion inputs

| n-Hexane | 0,3204 | MJfossil/MJ |
| --- | --- | --- |
| Phosphoric acid (H3PO4) | 28,57 | MJfossil/kg |
| Fuller's earth | 2,54 | MJfossil/kg |
| Hydrochloric acid (HCl) | 15,43 | MJfossil/kg |
| Sodium carbonate (Na2CO3) | 13,79 | MJfossil/kg |
| Sodium hydroxide (NaOH) | 10,22 | MJfossil/kg |
| Potassium hydroxide (KOH) | 0,00 | MJfossil/kg |
| Hydrogen (for HVO) | 1,4835 | MJfossil/MJ |
| Pure CaO for processes | 4,60 | MJfossil/kg |
| Sulphuric acid (H2SO4) | 3,90 | MJfossil/kg |
| Ammonia | 44,39 | MJfossil/kg |
| Cycle-hexane | 53,10 | MJfossil/kg |
| Lubricants | 53,28 | MJfossil/kg |

- Density

  - Density of liquid fuels (also conversion inputs)

| Diesel | 832 | kg / m3 |
| --- | --- | --- |
| Gasoline | 745 | kg / m3 |
| HFO | 970 | kg / m3 |
| HFO for marine transport | 970 | kg / m3 |
| Ethanol | 794 | kg / m3 |
| Methanol | 793 | kg / m3 |
| FAME | 890 | kg / m3 |
| Syn diesel (BtL) | 780 | kg / m3 |
| HVO | 780 | kg / m3 |

- Lower heating values (LHV’s)

  - Liquid and solid fuels (also conversion inputs)

| Diesel | 43,1 | MJ/kg (0% water) |
| --- | --- | --- |
| Gasoline | 43,2 | MJ/kg (0% water) |
| HFO | 40,5 | MJ/kg (0% water) |
| HFO for marine transport | 40,5 | MJ/kg (0% water) |
| Ethanol | 26,81 | MJ/kg (0% water) |
| Methanol | 19,9 | MJ/kg (0% water) |
| FAME | 37,2 | MJ/kg (0% water) |
| Syn diesel (BtL) | 44,0 | MJ/kg (0% water) |
| HVO | 44,0 | MJ/kg (0% water) |
| PVO | 36,0 | MJ/kg (0% water) |
| n-Hexane | 45,1 | MJ/kg (0% water) |
| Hard coal | 26,5 | MJ/kg (0% water) |
| Lignite | 9,2 | MJ/kg (0% water) |

  - Biofuel feedstocks and byproducts

| Corn | 18,5 | MJ/kg (0% water) |
| --- | --- | --- |
| FFB | 24,0 | MJ/kg (0% water) |
| Rapeseed | 26,4 | MJ/kg (0% water) |
| Soybeans | 23,5 | MJ/kg (0% water) |
| Sugar beet | 16,3 | MJ/kg (0% water) |
| Sugar cane | 19,6 | MJ/kg (0% water) |
| Sunflowerseed | 26,4 | MJ/kg (0% water) |
| Wheat | 17,0 | MJ/kg (0% water) |
| Animal fat | 37,1 | MJ/kg (0% water) |
| BioOil (byproduct FAME from waste oil) | 21,8 | MJ/kg (0% water) |
| Crude vegetable oil | 36,0 | MJ/kg (0% water) |
| DDGS (10 wt% moisture) | 16,0 | MJ/kg (10% water) |
| Glycerol | 16,0 | MJ/kg (0% water) |
| Palm kernel meal | 17,0 | MJ/kg (0% water) |
| Palm oil | 37,0 | MJ/kg (0% water) |
| Rapeseed meal | 18,7 | MJ/kg (0% water) |
| Soybean oil | 36,6 | MJ/kg (0% water) |
| Sugar beet pulp | 15,6 | MJ/kg (0% water) |
| Sugar beet slops | 15,6 | MJ/kg (0% water) |
| Wheat straw | 17,2 | MJ/kg (0% water) |

- Transport

  - Transport efficiencies

| Truck for dry product (Diesel) | 0,94 | MJ/ton,km |
| --- | --- | --- |
| Truck for liquids (Diesel) | 1,01 | MJ/ton,km |
| Truck for FFB transport (Diesel) | 2,01 | MJ/ton,km |
| Tanker truck MB2218 for vinasse (Diesel) | 2,16 | MJ/ton,km |
| Tanker truck with water cannons for vinasse (Diesel) | 0,94 | MJ/ton,km |
| Dumpster truck MB2213 for filter mud (Diesel) | 3,60 | MJ/ton,km |
| Ocean bulk carrier (Fuel oil) | 0,20 | MJ/ton,km |
| Ship /product tanker 50kt (Fuel oil) | 0,12 | MJ/ton,km |
| Local (10 km) pipeline | 0,00 | MJ/ton,km |
| Rail (Electric, MV) | 0,21 | MJ/ton,km |

  - Exhaust gas emissions from transport

| Truck for dry product (Diesel) | 0,005 | g CH4/ton,km | 0,0000 | g N2O/ton,km |
| --- | --- | --- | --- | --- |
| Truck for liquids (Diesel) | 0,005 | g CH4/ton,km | 0,0000 | g N2O/ton,km |
| Truck for FFB transport (Diesel) | 0,005 | g CH4/ton,km | 0,0000 | g N2O/ton,km |
| Tanker truck MB2218 for vinasse (Diesel) | 0,000 | g CH4/ton,km | 0,0000 | g N2O/ton,km |
| Tanker truck with water cannons for vinasse (Diesel) | 0,000 | g CH4/ton,km | 0,0000 | g N2O/ton,km |
| Dumpster truck MB2213 for filter mud (Diesel) | 0,000 | g CH4/ton,km | 0,0000 | g N2O/ton,km |
| Ocean bulk carrier (Fuel oil) | 0,000 | g CH4/ton,km | 0,0007 | g N2O/ton,km |
| Ship /product tanker 50kt (Fuel oil) | 0,000 | g CH4/ton,km | 0,0000 | g N2O/ton,km |
| Local (10 km) pipeline | 0,000 | g CH4/ton,km | 0,0000 | g N2O/ton,km |
| Rail (Electric, MV) | 0,000 | g CH4/ton,km | 0,0000 | g N2O/ton,km |